Modeling OF A Groundwater Circulation Well REMOVAL ACTION aLTERNATIVE

Gretchen R. Miller, EI, Assoc. Member, ASCE

Andrew Curtis Elmore, Ph.D., PE

ABSTRACT

This paper presents the basis for using groundwater circulation wells (GCWs) for removal actions focused on contaminated domestic water supplies. A properly placed GCW could be used to pre-treat water before it enters a domestic well.  Commercial software was used to develop a model for GCWs installed at a Nebraska Superfund site to perform a feasibility study of a GCW-based removal action.  Deterministic capture zone analysis provided guidance for locating vertically installed GCW up-gradient of an existing domestic well at the site.  A deviation of up to 7.6 m off-center of the hydraulic gradient may be permissible.  A GCW flow rate range to provide a sufficiently large recharge zone to protect a typical domestic well was identified for the site.  Stochastic analysis indicated that the system was sensitive to horizontally variable hydraulic conductivity.  Modeling results indicate that a GCW may both reduce contaminant mass in the aquifer, and act as a water supply replacement alternative to point of use treatment systems.

# Footnotes

Ph.D. Student, Department of Civil and Environmental Engineering, 760 Davis Hall, University of California-Berkeley, Berkeley, CA  94720-1710, gmiller@berkeley.edu

Assistant Professor, University of Missouri-Rolla, Department of Geological Engineering, 129 McNutt Hall, 1870 Miner Circle, Rolla, MO  65409-0420, 573-341-6784, elmoreac@umr.edu